## Slide 1: ACS Mid-Atlantic Regional Meeting Combined Heat and Power in Automobiles: Utilization of Waste Engine Heat to Drive Ethanol/Water Distillation
Benjamin D’Alessio, John Allen Rudesill and Douglas Frey
University of Maryland Baltimore County
Department of Chemical, Biochemical and Environmental Engineering
June 2, 2012

## Slide 2
Outline
  Project background
  Project proposal
  Design and components
  Results and system evaluation
  Practical considerations

## Slide 3: Project Background
Why do we care about using ethanol as an alternative fuel?

## Slide 4: Project Background: Why use ethanol?
  Environmental standpoint
    Ethanol is a clean-burning fuel that produces less greenhouse gas emissions than gasoline[1]
Energy independence standpoint
    Ethanol is currently used as a fuel additive and octane booster; has the potential to reduce the need for fossil fuels from foreign sources significantly[2]
    This fuel can be produced from corn and cellulosic sources grown here in the United States
[1] Wang et al. Effects of Fuel Ethanol Use on Fuel-Cycle Energy and Greenhouse Gas Emissions. U.S. DOE. 1999.
[2] Shapouri H. et al. The Energy Balance of Corn Ethanol: An Update. 2002.
Notes: citation

## Slide 5: Project Background: Ethanol Production
Six basic steps in manufacturing ethanol[1]
  Milling of corn
  Liquification
  Saccharification
  Fermentation
  Distillation
  Dehydration
[1] Kwiatkowski, J.R. et al. Modeling the process and costs of fuel ethanol production by the corn dry-grind process. 2005

## Slide 6: Project Background: Ethanol Production
Six basic steps in manufacturing ethanol[1]
  Milling of corn
  Liquification
  Saccharification
  Fermentation
  Distillation
  Dehydration
Most energy intensive steps
[1] Kwiatkowski, J.R. et al. Modeling the process and costs of fuel ethanol production by the corn dry-grind process. 2005

## Slide 7: Project Background: Ethanol Production
[1]
[3] Martinez-Frias et al. Improving Ethanol Life Cycle Energy Efficiency by Direct Utilization of Wet EtOH in HCCI engines. 2007

## Slide 8: Project Background: Improving Net Energy Value
  Use of wet ethanol in traditional internal combustion engines
    Modify fuel tank, fuel lines and carburetor to accommodate ethanol/water fuel[1]
    Pre-vaporization often necessary
    Mixtures of 90% EtOH and below have been tested
Homogeneous Charge Compression (HCCI) engines[2,3]
  Use ‘wet ethanol’ in concentrations as low as 35% EtOH by volume as fuel source
  Potential to decrease distillation requirement by 20% and complete elimination of dehydration step
  Not suitable yet for use in transportation vehicles
[1] Williams J. Steady-State dynamometer Testing of a Passenger Van: Comparing Operation on Gasoline and Aqueous Ethanol. 2004.
[2] Martinez- Frias, J. et al. Improving Ethanol Life Cycle Energy Efficiency by Direct Utilization of Wet Ethanol in HCCI Engines. 2007.
[3] Mack, J. et al. Direct Use of Wet Ethanol in a HCCI Engine: Experimental and Numerical Results. 2007.

## Slide 9: Project Proposal
What else can be done to increase the net energy value of ethanol as an automotive fuel?
9
Notes: 9

## Slide 10: Project Proposal: Utilize waste engine heat
Internal combustion engines have very low efficiency
  Between 60% and 80% of energy is dissipated as heat through the engine block or exits the tailpipe
  Close to 15% of mechanical energy reaches the wheels[1]
If ethanol is used as a primary fuel, its combustion energy can be used to do not only mechanical work but can also provide heat energy from combustion to drive its own distillation
This would allow lower purity ethanol to be produced at the production scale, thus limiting the distillation requirement and eliminating the need for dehydration
GOAL: Build a proof of concept and evaluate feasibility of implementation from an energetic and mechanical standpoint
[1] U.S. DOE. Advanced Technologies and Energy Efficiency. http://www.fueleconomy.gov/feg/atv.shtml.

## Slide 11: Energy Balance for 50% EtOH Production

## Slide 12: Engine and column schematic
Gasoline Startup
Engine
50 % v/v EtOH
90 % v/v EtOH
Exhaust
Bottoms
Heat Energy

## Slide 13: Start up mode
Gasoline Startup
Engine
50 % v/v EtOH
90 % v/v EtOH
Exhaust
Bottoms
Heat Energy

## Slide 14: Transfer to ethanol fuel
Gasoline Startup
Engine
50 % v/v EtOH
90 % v/v EtOH
Exhaust
Bottoms
Heat Energy

## Slide 15: Design and Components

## Slide 16: Overall Design Strategy of System
Load
Efficiency
Fuel consumption rate
Lower heating value of gasoline
EtOH equivalent rate
Desired distillate flow rate
Distillate flow rate
Feed composition/flow rate
Diameter/Height
Packing material
Reboiler and condenser duties
Heat energy needed
Heat energy available
Best method of transfer
Engine
Distillation Column
Heat Exchanger

## Slide 17: Engine Specifications
Displacement: 160 cc
Max Power Output: 2.5 kWh
Fuel Capacity: 3.9 gallons
Reasons for choosing generator set
  Runs at constant load delivering relatively constant exhaust temperature once steady state is reached
  Can vary based on load, and a range of loads was used during experimentation
  Muffler and components can easily be removed to accommodate longer exhaust piping for heat exchanger

## Slide 18: Determining Fuel Intake and Energy Output
Specification | Value | 
Load | 2.0 | kWh
Efficiency | 20 | %
Fuel capacity | 3.9 | gallons
Energy Used (same as load) | 6,824 | BTU/hr
Energy Needed (assuming 20% efficiency) | 34,120 | BTU/hr
Lower Heating Value | 116,090 | BTU/gal
Gasoline Consumption rate | 0.29 | gal/hr
EtOH Lower Heating Value | 76,330 | BTU/gal
Equivalent EtOH Consumption rate | 0.45 | gal/hr
Desired EtOH distillate rate | 0.50 | gal/hr

## Slide 19: Distillation Column Specifications
Distillate
Feed
Bottoms
Continuous distillation column material balance first calculated using Excel
Final design based on ChemSep model
Column Specifications (based on 50% v/v ethanol feed)
  Packed Column using stainless steel scrubbing pads as packing
  Temperature monitored using thermocouples
  Height: 10 feet
  Diameter: 1.5 inches
  HTEP: 13 centimeters

## Slide 20: Distillation Column Fabrication
20

## Slide 21: Distillation Column Material Balance: Excel

## Slide 22: Distillation Column: ChemSep Specifications
 | Feed | Top | Bottom
Stage | 9 | 1 | 12
Pressure (N/m2) | 101325 | 101325 | 101325
Temperature (K) | 300 | 350.9 | 366.0
Mole flows (kmol/s) |  |  | 
Ethanol | 8.84E-06 | 8.40E-06 | 4.42E-07
Water | 1.91E-05 | 2.37E-06 | 1.68E-05
Total molar flow | 2.80E-05 | 1.08E-05 | 1.72E-05
Mole fractions |  |  | 
Ethanol | 0.316 | 0.780 | 0.026
Water | 0.684 | 0.220 | 0.974

## Slide 23: Heat Exchanger Design Strategy

## Slide 24: Heat Exchanger Design Strategy
Gasoline Startup
Engine
50 % v/v EtOH
90 % v/v EtOH
Exhaust
Bottoms
1. How much energy is required?
2. How much energy can be delivered from heat of combustion?
3. What is the best method of transfer and regulation?

## Slide 25: How much heat is required?
50 % v/v EtOH
90 % v/v EtOH
Bottoms
Distillation column specifications
Feed: 50% EtOH
50% Water
Temperature: 300 K
Pressure: 1 atm
Distillate Flow rate: 0.50 gal/hr at 350 K
Reboiler duty: 6,950 BTU/hr

## Slide 26: How much energy can be delivered?
Engine
Gasoline
20 to 40 % mechanical and
electrical work
60 to 80% dissipated heat
For Honda EP2500CX
Assume : 20% efficiency
For gasoline, LHV: 116,090 BTU/gal
Available heat energy: 92,870 BTU/gal
Gasoline consumption rate: 0.30 gal/hr
Heat dissipation rate: 27,860 BTU/hr

## Slide 27: How much energy can be delivered?
Engine
Gasoline
20 to 40 % mechanical and
electrical work
60 to 80% dissipated heat
For Honda EP2500CX
Assume : 20% efficiency
For gasoline, LHV: 116,090 BTU/gal
Available heat energy: 92,870 BTU/gal
Gasoline consumption rate: 0.30 gal/hr
Heat dissipation rate: 27,860 BTU/hr

## Slide 28: How much energy can be delivered?
Engine
Gasoline
20 to 40 % mechanical and
electrical work
60 to 80% dissipated heat
For Honda EP2500CX
Assume : 20% efficiency
For gasoline, LHV: 116,090 BTU/gal
Available heat energy: 92,870 BTU/gal
Gasoline consumption rate: 0.30 gal/hr
Heat dissipation rate: 27,860 BTU/hr
Heat available to drive distillation almost 4x what is required
Heat Duty: 6,950 BTU/hr

## Slide 29: How much energy can be delivered?
Engine
Ethanol
20 to 40 % mechanical and
electrical work
60 to 80% dissipated heat
For Honda EP2500CX
Assume : 20% efficiency
For ethanol, LHV: 76,330 BTU/gal
Available heat energy: 61,060 BTU/gal
Ethanol consumption rate: 0.45 gal/hr
Heat dissipation rate: 27,500 BTU/hr

## Slide 30: How much energy can be delivered?
Engine
Ethanol
20 to 40 % mechanical and
electrical work
60 to 80% dissipated heat
For Honda EP2500CX
Assume : 20% efficiency
For ethanol, LHV: 76,330 BTU/gal
Available heat energy: 61,060 BTU/gal
Gasoline consumption rate: 0.45 gal/hr
Heat dissipation rate: 27,500 BTU/hr
Similar heat transfer rate as gasoline because fuel consumption was adjusted. Will probably be slightly lower since about 90% aqueous EtOH will
eventually be used.

## Slide 31: Methods of heat transfer and regulation
Direct Heating
  Copper tubing wrapped around exhaust pipe, reboiler contents recirculated through coiled tubing
  Pros: More efficient transfer of heat from exhaust gas to reboiler stream
  Cons: Control of heat not as easy, requires the need to pump high temperature water that could vaporize
Use of a heat exchange medium
  Ethylene glycol recirculated through coiled tubing
  Pros: Better control through regulating circulation rate, normal boiling point 197C.
  Cons: Less efficient as there will be inherent heat losses in pumping and transfer to reboiler
[1] GFX Heat Exchanger. Retrived from http://www.achrnews.com/Articles/Feature_Article/392ce1c95795a010VgnVCM100000f932a8c0
[1]

## Slide 32: Design methods

## Slide 33: Exhaust Heat Integration
33

## Slide 34: Final Design Specifications
  Distillate purity of 90 % v/v
  Distillate flow rate of 0.50 gal/hour
  Effective Heat Capture using plate and frame heat exchanger
34

## Slide 35: System Evaluation
What really matters?

## Slide 36: Phase I: Distillation Column Fabrication
  Column Height reduced to about 10 feet overall, with about 7 feet of packing
  Heat supplied initially using a 1500W heating element
    Initial testing showed too much heat was present, despite reboiler duty of 2040W
    Used a Variac to reduce heat input
  Reboiler design likely affected how heat was distributed to reboiler contents – probable vapor pocket formation that resulted in flooding

## Slide 37: Phase I: Distillation Column Fabrication
  Continuous distillation proved to be too difficult to control – erratic purity and distillate flow rate
    Required finding optimal feed flow rate, reflux return rate and heat input that didn’t produce flooding
  Continuous column was converted to batch column
    Provided much more consistent results with heating element
    Control of top temperature mainly achieved by adjusting heat input to reboiler
    Although heat input did impact distillate flow rate, this was mainly controlled by reflux return rate
    Overall distillate flow rate and purity determined at end of run

## Slide 38: Phase II: Exhaust Heat Integration
  Initially created a mock setup to recirculate water through heat exchanger connected to engine exhaust outlet and vaporize to determine if enough heat was present
    Used two centrifugal pumps connected in series
    Discovered temperature drop across muffler was nearly 200C; muffler was removed and exchanger was connected directly to engine cylinder outlet
    Modification provided necessary heat to create desired vapor flow rate
  Coupled distillation column to heat exchanger

## Slide 39: Phase II: Exhaust Heat Integration

## Slide 40: Phase III: Modify engine to run on 90% EtOH
  Couple distillation column to exhaust heat using final design of heat exchanger
  Perform several runs evaluating whether enough heat is present based on exchanger calculations and flow rates of exhaust and heat exchange medium
  Based on attainable outputs of distillate, overall feasibility of implementing the apparatus will be evaluated

## Slide 41: Evaluating the system: What really matters?

## Slide 42: Consider the following…
  How well does the system in its current setup work? What are the determining factors of success?
    Distillate purity and flow rate
    Ease of control
  How do the expected results compare with the actual results?
  What are the implications of any discrepancies?
  What factors affect the performance of the column?
    Heat input
    Reflux ratio
    Overall layout of column
    Prevailing ambient conditions

## Slide 43: Noted trends in column performance
  Heat input that is too high leads to instability
    Column flooding and compromised distillate purity
  Continuous distillation mode too difficult to control – transfer to batch mode proved to be more stable
  Heat input must be increased for consistent distillation to occur in the batch mode
  Too high reflux return also produces flooding
  Average engine loads on the lower end results in high purity; too low and not enough vapor is produced however

## Slide 44: Effect of high heat input
Chart: Batch Distillation using 50% v/v EtOH charge (Average Engine Load: 1650 Watts)

## Slide 45: Effect of low heat input

## Slide 46: Optimal purity attained at engine loads ~1200W
Chart: Distillate purity vs. Engine load
| 1560 | 1648 | 1249 | 1048 | 1294 | 1230 | 1232 | 1275 | 1232
 | 89.5 | 91 | 93.5 | 80 | 88 | 96 | 92 | 90 | 95

## Slide 47: Distillate Flow Rate 15-20 mL/min
Chart: Distillate flow rate vs. Engine load
| 1560 | 1648 | 1249 | 1048 | 1294 | 1230 | 1232 | 1275 | 1232
 | 16.4064 | 24.3493 | 15.1468 | 21.1509 | 15.6422 | 18.8613 | 17.95 | 18.0572 | 14.5699

## Slide 48: Integrated Heat Exchanger Temperature Profile
Exhaust Inlet
To Reboiler
Exhaust Outlet
From
Reboiler
Chart: Time (hours : minutes)
| 0 | 1.3888888861401938E-3 | 2.7777777286246419E-3 | 4.1666666293167509E-3 | 5.5555555300088599E-3 | 6.944444430700969E-3 | 8.333333331393078E-3 | 9.722222232085187E-3 | 1.1111111132777296E-2 | 1.2499999931605998E-2 | 1.3888888832298107E-2 | 1.5277777732990216E-2 | 1.6666666633682325E-2 | 1.8055555534374435E-2 | 1.9444444427790586E-2 | 2.0833333328482695E-2 | 2.2222222134587355E-2 | 2.3611111028003506E-2 | 2.4999999928695615E-2 | 2.6388888829387724E-2 | 2.7777777730079833E-2 | 2.9166666630771942E-2 | 3.0555555531464051E-2 | 3.1944444330292754E-2 | 3.3333333230984863E-2 | 3.4722222131676972E-2 | 3.6111111032369081E-2 | 3.749999993306119E-2 | 3.8888888833753299E-2 | 4.0277777734445408E-2 | 4.1666666627861559E-2 | 4.3055555433966219E-2 | 4.4444444334658328E-2 | 4.583333322807448E-2 | 4.7222222128766589E-2 | 4.8611111029458698E-2 | 4.9999999930150807E-2 | 5.1388888830842916E-2 | 5.2777777629671618E-2 | 5.4166666530363727E-2 | 5.5555555431055836E-2 | 5.6944444331747945E-2 | 5.8333333232440054E-2 | 5.9722222133132163E-2 | 6.1111111033824272E-2 | 6.2499999832652975E-2 | 6.3888888733345084E-2 | 6.5277777634037193E-2 | 6.6666666534729302E-2 | 6.8055555428145453E-2 | 6.9444444328837562E-2 | 7.0833333229529671E-2 | 7.2222222028358374E-2 | 7.3611110929050483E-2 | 7.4999999829742592E-2 | 7.6388888730434701E-2 | 7.777777763112681E-2 | 7.9166666531818919E-2 | 8.0555555432511028E-2 | 8.1944444333203137E-2 | 8.3333333132031839E-2 | 8.4722222032723948E-2 | 8.6111110933416057E-2
Exhaust Out | 37.3 | 45.8 | 53 | 58 | 61 | 62.5 | 66.4 | 70.3 | 72.7 | 74.2 | 75.4 | 76.1 | 76.4 | 76.8 | 77.6 | 78 | 78.6 | 79.2 | 79.5 | 79.8 | 80.1 | 80.2 | 80.5 | 80.7 | 81 | 81.3 | 81.6 | 81.9 | 82.2 | 82.7 | 82.7 | 83.7 | 83.7 | 84 | 84.8 | 84.8 | 85.3 | 85.5 | 85.6 | 85.7 | 85.2 | 85.4 | 85.4 | 85.3 | 85.3 | 85.5 | 85.9 | 86.6 | 86.8 | 87.4 | 88 | 88.7 | 89.2 | 89.7 | 90 | 90.5 | 90.8 | 91.3 | 81.4091
Water in | 41.2 | 50.6 | 57 | 62.5 | 67.3 | 72.5 | 78.6 | 83.5 | 86.7 | 87 | 87.5 | 87.7 | 87.9 | 88.2 | 88.6 | 89 | 89.3 | 89.6 | 89.9 | 90.2 | 90.5 | 90.6 | 90.8 | 91 | 91.2 | 91.6 | 91.8 | 92.1 | 92.5 | 92.9 | 93.1 | 93.5 | 94.2 | 94.6 | 94.9 | 95.2 | 95.4 | 95.6 | 95.8 | 95.8 | 95.7 | 95.7 | 95.6 | 95.5 | 95.7 | 95.8 | 96.1 | 96.4 | 97.4 | 98 | 98.6 | 99.5 | 100 | 100.6 | 101 | 101.5 | 101.7 | 102 | 91.9255
Water out | 36.2 | 42.9 | 49.2 | 56.2 | 61.5 | 66.2 | 71.9 | 76.4 | 79.2 | 80.6 | 81.2 | 81.3 | 81.5 | 81.9 | 82.3 | 82.3 | 83 | 83.2 | 83.5 | 83.3 | 84.1 | 84.3 | 84.6 | 84.8 | 85.1 | 85.3 | 85.7 | 86 | 86.4 | 86.9 | 87 | 87.4 | 87.7 | 88.2 | 88.5 | 88.9 | 89.2 | 89.5 | 89.7 | 89.9 | 89.8 | 89.5 | 89.2 | 89.2 | 89.2 | 89.3 | 89.5 | 89.7 | 90.2 | 90.8 | 91.3 | 91.9 | 92.7 | 93.2 | 93.8 | 94.1 | 94.6 | 94.8 | 95.2
Exhuast In | 363 | 447 | 477 | 495 | 503.6 | 508.3 | 510 | 512 | 510 | 500 | 498 | 497.8 | 497.5 | 497.8 | 496.8 | 496.8 | 496 | 497.8 | 496.6 | 495 | 495 | 495 | 495 | 495.4 | 495.7 | 495.7 | 495.2 | 494.8 | 495 | 493.8 | 494.4 | 494.7 | 494 | 494.7 | 494.1 | 494.2 | 493.2 | 494.4 | 493.5 | 494 | 494.7 | 496 | 499.2 | 499.7 | 501.8 | 501.9 | 502.8 | 503.6 | 504.6 | 504.4 | 504.8 | 504.6 | 506 | 506.9 | 506.9 | 506.3 | 507 | 507 | 507 | 499.3929

## Slide 49: Final Results: Were design goals met?
  Distillate purity of 90 % v/v
  Distillate flow rate of 0.50 gal/hour
    Column was able to consistently produce 90 % or greater purity at 0.24 – 0.32 gal/hr
    Even at lower loads, distillate flow rate could not match or exceed equivalent ethanol consumption rate
    Larger column needed to provide necessary flow rate
  Effective Heat Capture
    Use of plate and frame heat exchanger provided adequate heat exchange
    Likely not all of heat exchanger area was utilized
    Recirculation of reboiler contents allowed for flashing to occur, precise control needs further development

## Slide 50: Practical Considerations
Is it feasible?

## Slide 51: Yes, but with some considerations…
  Scale-up of column
  Column height restrictions
  Control of heat
  Inertial forces on column and the effect on performance and efficiency
  Weight: Need nearly twice the volume of fluids
    Tankage for gasoline and reserve ethanol
  Revamp of fuel delivery infrastructure
  Short trip dilemma

## Slide 52: Acknowledgements
  ACS
  John Rudesill
  Dr. Frey
  Dr. Castellanos
  Dr. Kostov
  Dr. Bayles
  Robert Henderson

## Slide 53: Questions?